## Slide 1: Logic and computers

## Slide 2: Binary Arithmetic
0
+ 0
----
0
0
+ 1
----
1
1
+ 0
----
1
1
+ 1
----
10
Only two digits: the bits 0 and 1
(Think: 0 = F, 1 = T)

## Slide 3: Logic and Computers
A half adder:
  Two bits in (A, B: to be added together)
  Two bits out (S, C: sum and carry)
  0+0=0, carry 0
  0+1=1, carry 0
  1+0=1, carry 0
  1+1=0, carry 1
S := A⊕B
C := A∧B

## Slide 4
NOT
OR NOR
AND NAND
XOR NXOR
(EQUIV)
LOGIC GATES

## Slide 5: Logic and Computers
S := A⊕B
C := A∧B
A
S
B
C

## Slide 6: Half Adder
A S
B C
HA
A
S
B
C

## Slide 7: A Longer Addition
11
+ 11
1
0
1
1
1

## Slide 8: Full Adder
Need a third input to create a component of a ripple-carry adder: the carry from the previous bit position
Inputs: A, B, Cin
Outputs: S, Cout
A | B | Cin | S | Cout
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1

## Slide 9: Full Adder
A | B | Cin | S | Cout
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1
A
B
Cin S
Cout
HA
HA
A S
B C
HA

## Slide 10: Full Adder
Cin
S
A
B Cout
FA
A
B
Cin S
Cout
HA
HA

## Slide 11: Ripple carry adder
2-bit adder: a1a0+b1b0 = c1c0 with carryout
Generalizes to n-bit addition
How does the time delay through the circuit depend on n, the number of bits to be added?
0
a0
b0
a1
b1
c0
c1
carryout
FA
FA

## Slide 12: Clever faster 2n-bit adder
To beat 2n carry delays from adding two 2n-bit numbers:
Have three n-bit adders do their work simultaneously:
  Low order n bits of the two addends
  High order n bits of the two addends, with carry-in = 0
  High order n bits of the two addends, with carry-in = 1
Use the carry-out of a) to select between the result of b) and c)
  (A∧B) ⋁ (¬A∧C)

## Slide 13: Simplifying Circuits
Simpler formulas turn into circuits that use less hardware!
E.g. p ⋁ q ⋁ (p⋀q) is equivalent to p ⋁ q but would use more logic gates
But the P=NP? question means that it may be hard to simplify formulas as much as possible
  Any tautology is equivalent to p ⋁ ¬p so if we could easily simplify formulas we could easily determine whether a formula is a tautology

## Slide 14: FINIS